How to Use the Michigan Neuropathy Screening Instrument

History

The history questionnaire is self-administered by the patient.  Responses are added to obtain the total score.  Responses of “yes” to items 1-3, 5-6, 8-9, 11-12, 14-15 are each counted as one point.  A “no” response on items 7 and 13 counts as 1 point.  Item #4 is a measure of impaired circulation and item #10 is a measure of general aesthenia and are not included in scoring.  To decrease the potential for bias, all scoring information has been eliminated from the patient version.

Physical Assessment

For all assessments, the foot should be warm (>30(C).

Foot Inspection:  The feet are inspected for evidence of excessively dry skin, callous formation, fissures, frank ulceration or deformities.  Deformities include flat feet, hammer toes, overlapping toes, halux valgus, joint subluxation, prominent metatarsal heads, medial convexity (Charcot foot) and amputation.

Vibration Sensation:  Vibration sensation should be performed with the great toe unsupported.  Vibration sensation will be tested bilaterally using a 128 Hz tuning fork placed over the dorsum of the great toe on the boney prominence of the DIP joint.  Patients, whose eyes are closed, will be asked to indicate when they can no longer sense the vibration from the vibrating tuning fork.

In general, the examiner should be able to feel vibration from the hand-held tuning fork for 5 seconds longer on his distal forefinger than a normal subject can at the great toe (e.g. examiner’s DIP joint of the first finger versus patient’s toe).  If the examiner feels vibration for 10 or more seconds on his or her finger, then vibration is considered decreased.  A trial should be given when the tuning fork is not vibrating to be certain that the patient is responding to vibration and not pressure or some other clue.  Vibration is scored as 1) present if the examiner senses the vibration on his or her finger for < 10 seconds, 2) reduced if sensed for ( 10 or 3) absent (no vibration detection.)

Muscle Stretch Reflexes: The ankle reflexes will be examined using an appropriate reflex hammer (e.g. Trommer or Queen square).  The ankle reflexes should be elicited in the sitting position with the foot dependent and the patient relaxed.  For the reflex, the foot should be passively positioned and the foot dorsiflexed slightly to obtain optimal stretch of the muscle.  The Achilles tendon should be percussed directly.  If the reflex is obtained, it is graded as present.  If the reflex is absent, the patient is asked to perform the Jendrassic maneuver (i.e., hooking the fingers together and pulling).  Reflexes elicited with the Jendrassic maneuver alone are designated “present with reinforcement.”  If the reflex is absent, even in the face of the Jendrassic maneuver, the reflex is considered absent.

Monofilament Testing:  For this examination, it is important that the patient’s foot be supported (i.e., allow the sole of the foot to rest on a flat, warm surface).  The filament should initially be prestressed (4-6 perpendicular applications to the dorsum of the examiner’s first finger).  The filament is then applied to the dorsum of the great toe midway between the nail fold and the DIP joint.  Do not hold the toe directly.  The filament is applied perpendicularly and briefly, (<1 second) with an even pressure.  When the filament bends, the force of 10 grams has been applied.  The patient, whose eyes are closed, is asked to respond yes if he/she feels the filament.   Eight correct responses out of 10 applications is considered normal: one to seven correct responses indicates reduced sensation and no correct answers translates into absent sensation.